# IP source guard
## Purpose
FastDPI BNG verifies the consistency between subscriber VLAN tags and the subscriber IP address.
When assigning an IP address via DHCP, FastDPI BNG stores the subscriber VLAN/QinQ tags in the built-in UDR database. These data are later used to validate the correspondence between the packet source IP and its VLAN tags.
IP source guard is applied only to outbound traffic (LAN → WAN).
## Enabling the mode
To activate, set the parameter bras_ip_source_guard in the fastdpi.conf file:
- 0 — mode disabled (default)
- 1 — mode enabled and applied only to active sessions
If after restarting fastDPI the session state is unknown, IP source guard is not applied and the packet is allowed.
## Packet processing logic
With bras_ip_source_guard=1, a packet is allowed if:
- the session is active and the packet VLAN tags match the tags registered during DHCP
- the session status is unknown
In all other cases, the packet is dropped.
## AS-based termination mode
The AS-based termination mode is available.
In this mode, IP source guard is applied only to source IP addresses whose AS is marked with the term flag.
## Filtering by source AS flags
Additional filtering of subscriber traffic by AS flags is supported in the subs → inet direction before packet processing. The mechanism is intended to block outbound DDoS traffic with spoofed IP addresses originating from the operator network.
The parameter ip_filter_source_as_flags (hot) is used in fastdpi.conf.
Only packets whose source IP AS contains at least one of the specified flags are allowed for processing. Otherwise, the packet is dropped.
Flag values (bitmask):
- 0 — filtering disabled (default), ip_filter_source_as_flags=0x0
- 0x0100 — pass
- 0x0200 — local
- 0x0400 — peer
- 0x0800 — term
- 0x1000 — mark1
- 0x2000 — mark2
- 0x4000 — mark3