# Setting the termination parameters for each output DPDK interface
Warning: this feature should be used after careful consideration. Often, instead of specifying special options for output interfaces, you need to revisit the network topology.

In the VAS Experts DPI 7.4+ a new feature to specify termination parameters for each output DPDK interface on your own is added. The bras_term_dev_outer option is used for this purpose:
   # The option sets the termination modes for the particular output interface
bras_term_dev_outer=dev=41-00.1;bras_gateway_ip=188.227.73.41;bras_gateway_mac=00:e0:ed:43:84:41;bras_vlan_terminate=1;bras_vlan_subst=1907;bras_terminate_l2=1
Here dev specifies the name of the DPDK output interface, the other parameters are used to define this output interface. The following termination options can be specified:
- bras_gateway_ip
- bras_gateway_mac
- bras_vlan_terminate
- bras_vlan_subst
- bras_terminate_l2
For each output interface its options can be specified by a new line
bras_term_dev_outer=dev=41-00.1;bras_gateway_ip=188.227.73.41;bras_gateway_mac=00:e0:ed:43:84:41;bras_vlan_terminate=1;bras_vlan_subst=1907;bras_terminate_l2=1
bras_term_dev_outer=dev=42-00.1;bras_gateway_ip=188.100.10.101;bras_gateway_mac=45:10:10:55:39:e5;bras_vlan_terminate=3;bras_vlan_subst=666;bras_terminate_l2=1
If the bras_term_dev_outer option is not specified for the output interface, then the corresponding global settings are used for it.
All the needed termination options should be specified within the bras_term_dev_outer option. The VAS Experts DPI does not compound the global termination options and options that are specific for the particular interface.