# FastPCRF (BRAS integration by RADIUS)
PCRF provides proxying requests from fastDPI to the Radius server. It is a part of the standard Stingray Service Gateway installation package, but if necessary, it can be used as a dedicated server.
## Hardware Recommendations
In order to run PCRF you can use the following hardware or virtual machines matching the following characteristics:
1. CPU 2.5 GHz, 1 pcs
2. RAM 512 MB - 1 GB
3. HDD 50 GB - 250 GB
4. Operating system Cent OS 8.5, VEOS
5. NIC ranging from 10 Mb/s
## Installation
1. Install the Network Time Protocol daemon
  yum install chrony -y
  systemctl restart chronyd
  timedatectl
  When entering the timedatectl command, the System clock synchronized parameter must be set to yes
2. Add vasexperts repository
  rpm --import http://vasexperts.ru/centos/RPM-GPG-KEY-vasexperts.ru
  rpm -Uvh http://vasexperts.ru/centos/6/x86_64/vasexperts-repo-2-1.noarch.rpm
3. Install the fastPCRF
  yum install fastpcrf
4. Make sure the service is running
  service fastpcrf start
5. Сonfigure fastpcrf service to run at startup
  systemctl enable fastpcrf
6. Open firewall ports in order to access the fastPCRF and Radius servers
  firewall-cmd --permanent --zone=public --add-port=22/tcp
  firewall-cmd --permanent --zone=public --add-port=3799/udp
  firewall-cmd --permanent --zone=public --add-port=29002/tcp
and restart firewall for the rules to take effect
firewall-cmd --reload
Disable selinux [1)]
[1)] temporary solution
setenforce 0
vi /etc/selinux/config
SELINUX=disabled
## Installation of the fdpi_cli and fdpi_ctrl utilities on the PCRF server
You can get these utilities from the server where fastDPI is installed.
The utility files are located in /usr/sbin/.
1. Copy the utilities to the home directory
  cp /usr/sbin/fdpi_cli /home/vasexpertsmnt
  cp /usr/sbin/fdpi_ctrl /home/vasexpertsmnt
2. Move these files to the server where fastPCRF is installed, to /home/vasexpertsmnt
How to use the utility:
fdpi_cli -r 1.1.1.1 dpi config get trace_ip
fdpi_cli -r 2.2.2.2 pcrf config get verbose
fdpi_ctrl -r 1.1.1.1:29000 list all --bind
Server address – 1.1.1.1 where the fastDPI module is installed.
Server address – 2.2.2.2 where the fastPCRF module is installed.