# Database administration
UDR (built-in database, user data repository) is used for permanent storage of data on services and policing settings for the subscribers.
List of database tables
Table	Purpose
bindings	login and address binding
bindings_multi	login and address binding for multu-subscribers (with several IPs)
policing	Subscriber policing setting
profile_names	Names of profiles
profiles	Profiles of services and policing
services	Subscriber services setting
vchannel_policing	Channel policing setting
ip_props	BRAS subscriber properties

### Activating the built-in database
UDR activation is required to support dynamic IPs and subscribers with several IPs.

UDR is activated by the configuration parameter in /etc/dpi/fastdpi.conf file.
udr=1
The created database is located in the /var/db/dpi directory
You can make a copy of the database without stopping the DPI with a backup command / mdb_copy/var/db/dpi./DB / and handle further manipulations in the copied database.

### Enlarging the DB
By default, the database size is limited to 1GB. If you have more than 1 million policing profiles, you will need to increase the default size:
udr_size=2147483648
will set the DB size of 2GB.
The built-in database does not require administration and is fault tolerant. However, in rare cases, damage to the embedded database occurred. In this case, one of the following options is possible.

### Database recovery with data transfer
Stop the fastDPI
service fastdpi stop
Run the script
rm -rf /var/db/dpi.recover/*
mkdir -p /var/db/dpi.recover/tmp
for table in $(mdb_dump -l /var/db/dpi); do
mdb_dump -f /var/db/dpi.recover/tmp/dump.$table.load -s $table /var/db/dpi
mdb_load -f /var/db/dpi.recover/tmp/dump.$table.load /var/db/dpi.recover
done
rm /var/db/dpi/lock.mdb
mv /var/db/dpi/data.mdb /var/db/dpi.recover/data.mdb.backup
cp -f /var/db/dpi.recover/data.mdb /var/db/dpi/
Start the fastDPI
service fastdpi start
### Deleting a database and reloading data back from an external source (billing, etc.)
Stop the fastDPI
service fastdpi stop
Delete the DB
/bin/rm /var/db/dpi/*
Start the fastDPI
service fastdpi start
Reload all the settings into the database using own scripts.
## Experimental Section
### Restoring a database to the fdpi_ctrl command format
Stop the fastDPI
service fastdpi stop
Run the script
mdb_dump -p -a -f dump.sh /var/db/dpi
/bin/rm /var/db/dpi/*
Start the fastDPI
service fastdpi start
Run the script
chmod +x dump.sh
./dump.sh
### Restoring certain tables to the fdpi_ctrl command format
Stop the fastDPI
service fastdpi stop
Run the script
for table in $(mdb_dump -l /var/db/dpi); do
mdb_dump -p -f dump.$table.sh -s $table /var/db/dpi
done
/bin/rm /var/db/dpi/*
Start the fastDPI
service fastdpi start
Choose and run the scripts you need, for example
chmod +x dump.bindings.sh
./dump.bindings.sh