# Monitoring via SNMP agent (Zabbix-agent)
We offer you the following set of parameters that can be taken from the SSG DPI:
- Errors in fastDPI process log /var/log/dpi/fastdpi_alert.log
- Errors in the /var/log/messages system log
- Losses (Drop) on dna interfaces
- Traffic volume on interfaces
- Availability of control interfaces
- Number of HTTP and HTTPS requests processed
- Number of blocked resources by HTTP, HTTPS, IP
- Number of PPPoE sessions
You can use Zabbix Agent for monitoring.
Current and final supported version of agent and server is 6.0, Zabbix agent 1 should be used. For newer versions of Zabbix, monitoring will be done via SNMP.
## Agent Setup
1. Install Zabbix agent 1 on the DPI server according to the instructions on the Zabbix website.
   In the first step, select the following values:
  1. Zabbix Packages
  2. Zabbix version: 6.0+
  3. OS distribution: CentOS
  4. OS version: 8 STREAM
  5. Zabbix component: AGENT
2. Edit the configuration file /etc/zabbix/zabbix_agentd.conf: change the parameters Server= and ServerActive= to your server address, hostname= to the server hostname.
3. Change the context of the /var/log/dpi/fastdpi_stat.log file:
chcon unconfined_u:object_r:zabbix_log_t:s0 /var/log/dpi/fastdpi_stat.log

2. Open tcp/udp ports 10050 and 10051 in firewall
3. Upload the ssg_userparams.conf file to the /etc/zabbix/zabbix_agent.d/ directory
4. Edit the ssg_userparams.conf file by replacing the interface number in UserParameter
   02-00.0 should be replaced with the interface names of your server!
   The name must match the DPI config. If you have more than 2 interfaces in use, you must add a line similar to the existing parameters.
UserParameter=dpi.02-00.0.drops,tac /var/log/dpi/fastdpi_stat.log | sed /'IF 02-00.0'/q | tac | sed -e 1,/'Actual Stats'/d | sed '6!D' | awk '{print $1}' | sed 's/^.//'

2. Restart the agent: systemctl restart Zabbix-agent
## Server setup
1. Install and configure Zabbix servers according to the instructions on the official website.
2. Add template zbx_export_templates.xml
   1) Go to Configuration section
   2) Templates section
   3) Click “Import”
   4) Import template file
   5) Save changes
3. Add a DPI server as a host
   1) Go to Monitoring section
   2) Hosts section
   3) Click “Create host”
   4) Set the required parameters, hostname, group and the previously added template
   5) Save changes
4. Edit the template: change the names of the interfaces and keys so that they match the UserParameter.