# Policing Management
Subscriber management is performed using the utility fdpi_ctrl.
We recommend using Named profiles, which simplifies policing management.

## Command Syntax
The general format of commands:
fdpi_ctrl command --policing policing_description_file [IP_list] [LOGIN_list]

Explanation of command parameters:
Parameter	Description, possible values, and format	Note
command	Values: 1. load — load data 2. del — delete. For --service, you need to specify the service_identifier 3. list — display information for the specified IP_list or all information if the all argument is provided.	In list and del commands, instead of an IP/LOGIN list, you can specify all, meaning the command will apply to all.
policing_description_file	A file in cfg format, e.g., tbf.cfg
IP_list	Values: 1. --file — file with a list of IPs 2. --ip — single IP, format: 192.168.0.1 3. --ip_range — IP range (inclusive), format: 192.168.0.1-192.168.0.5 4. --cidr — IP with port, format: 192.168.0.0/30, 5.200.43.0/24~ (CIDR format with excluded boundary addresses)	Boundary addresses can be excluded from a CIDR range (following the classless addressing agreement — gateway and broadcast addresses) by adding the ~ symbol at the end of the CIDR definition, e.g., --cidr 5.200.43.0/24~.
LOGIN_list	Values: 1. --file — file with a list of logins 2. --login — single login, format: USER1, "FIRST_NAME LAST_NAME" (alternative for specifying a login with escaped special characters)	"USER1" — option for specifying login in double quotes 'USER2' — option for specifying login in single quotes

A line starting with # is a comment.

## Examples
Enable policing policy using a policing description file:
fdpi_ctrl load --policing tbf.cfg --ip 192.168.0.1

2. Get a list of applied policing:
fdpi_ctrl list all --policing

2. Get information for a specific IP:
fdpi_ctrl list --policing --ip 192.168.0.1

2. Enable policing policy using a named profile:
fdpi_ctrl load --policing --profile.name tariff_10 --login kv_111