# Disk Space Configuration
QoE Stor uses several folders for storage:
- /var/qoestor/backend/dump – temporary data received by receivers is stored here. After being loaded into the database, this data is deleted.
- /var/lib/clickhouse/ - the so-called DEFAULT disk. Here, the database schema and data (raw and aggregated logs) are stored.
- /var/lib/clickhouse-hot/ - the so-called HOT disk.
- /var/lib/clickhouse-cold/ - the so-called COLD disk.
HOT and COLD disks are used when storage system cost reduction is needed.
DEFAULT must be very fast (e.g., NVMe SSD) to receive data from DPI, save it to the database in raw logs, and aggregate it (form aggregated logs).
The HOT disk can store aggregated logs for 1-2 weeks. The HOT disk should also be an SSD to quickly generate reports.
The COLD disk can store old data. COLD can be a SATA HDD disk, as reports on old data are rarely generated, and data can be stored on a slow disk.
For instructions on physically separating directories across disks, see below in the section Configuring Storage on a Separate Disk.
## Configuring Storage on a Separate Disk
By default, all data is stored in the /var partition.
Assume we have mounted a separate disk to /storage.
1. Work as the root user:
  sudo su
2. Stop the receivers and database:
  fastor-stop
  fastor-db-stop
3. Create directories in the /storage partition:
  mkdir /storage/qoestor
  mkdir /storage/qoestor/clickhouse
  mkdir /storage/qoestor/clickhouse-hot
  mkdir /storage/qoestor/clickhouse-cold
  mkdir /storage/qoestor/dump
4. Copy data to the new disk:
  cp -r /var/lib/clickhouse/* /storage/qoestor/clickhouse
  cp -r /var/lib/clickhouse-hot/* /storage/qoestor/clickhouse-hot
  cp -r /var/lib/clickhouse-cold/* /storage/qoestor/clickhouse-cold
  cp -r /var/qoestor/backend/dump/* /storage/qoestor/dump
5. Change the owner of the /storage/qoestor/clickhouse folder:
  chown -R clickhouse:clickhouse /storage/qoestor/clickhouse
  chown -R clickhouse:clickhouse /storage/qoestor/clickhouse-hot
  chown -R clickhouse:clickhouse /storage/qoestor/clickhouse-cold
6. Remove the old directories:
  rm -rf /var/lib/clickhouse
  rm -rf /var/lib/clickhouse-hot
  rm -rf /var/lib/clickhouse-cold
  rm -rf /var/qoestor/backend/dump
7. Create symlinks:
  ln -s /storage/qoestor/clickhouse /var/lib/clickhouse
  ln -s /storage/qoestor/clickhouse-hot /var/lib/clickhouse-hot
  ln -s /storage/qoestor/clickhouse-cold /var/lib/clickhouse-cold
  ln -s /storage/qoestor/dump /var/qoestor/backend/dump
8. Check the links:
  readlink -f /var/lib/clickhouse
  readlink -f /var/lib/clickhouse-hot
  readlink -f /var/lib/clickhouse-cold
  readlink -f /var/qoestor/backend/dump
9. Start the database:
  fastor-db-restart
10. Start the receivers:
  fastor-restart