# Hardware Requirements, Installation, and Update
## Minimum Hardware Requirements
FastRADIUS can be installed on a SCAT server or on a dedicated server or VM.
1. CPU — 2 cores
2. RAM — from 1 GB
3. SSD — 50 GB
4. Operating System — VEOS
   When selecting hardware, take into account the information in VEOS Update Notes.
5. Network Interface Card (NIC) — 2 ports, for SSH management (+ optional IPFIX sending) and for receiving RADIUS traffic
## Installation and Update
The component is included in the standard SSG software package. If used on the same server as SSG, no additional installation is required.
Further updates are performed in the standard way:
yum update fastradius
### Installation on a Separate Server or VM
1. Configure precise time synchronization via the ntpd service. NTPD configuration file: /etc/sysconfig/ntpd. To do this, install the precise time service
  yum install chrony -y
  systemctl restart chronyd
  timedatectl
  When running the timedatectl command, the System clock synchronized parameter must have the value yes
2. Connect the vasexperts repository
  rpm --import http://vasexperts.ru/centos/RPM-GPG-KEY-vasexperts.ru
  rpm -Uvh http://vasexperts.ru/centos/6/x86_64/vasexperts-repo-2-1.noarch.rpm
3. Install FastRADIUS
  yum install fastradius
4. Start the service
  systemctl start fastradius
5. Enable service autostart at boot
  systemctl enable fastradius
6. Check the status (should be running)
  systemctl status fastradius