# Description and hardware requirements
Radius events monitor is designed to send to DPI the information on assignment and release of subscribers' IP addresses in networks using dynamic IP assignment[1)]. It can control DPI servers capable to process a traffic of 100 million subscribers[2)].
[1)] Information transfer on policing services and settings via additional Radius attributes is under development
[2)] Radius events monitor is currently in use by Rostelecom network
Radius events monitor runs on a general purpose computer. However, due to deep code optimization and integration with the hardware, the hardware configuration has to meet some specific requirements:
1. CPU has 2 kernels or more.
2. Network cards on chipsets Intel 82575/82576/82580/82599 or x540 with 1, 2, 4 or 6 ports.
3. Any network adapter to handle control connection by SSH (usually the motherboard integrated one is OK).
Radius events monitor runs under VEOS.