# Assigning priorities according to the protocols
The protocol priorities (assigned by system administrator) are loaded by DPI from the file /etc/dpi/protocols.dscp.
This file is created in two steps: first one creates a text file with the list of protocols and their priorities. Second, it is converted into an internal format by a special utility.
To apply the changes you need to the DPI configuration with the following command:
service fastdpi reload
## The file format of protocols and priorities list:
Each line contains the protocol name, then space, then dscp value. For example:
dns 0x3F
skype drop
compressnet 010
ftp keep
http cs0
default keep
Full list of protocols. DSCP value is specified as decimal, hex or octal number or as a text abbreviation.

Keywords meaning:
- drop - indicates that packets must not be transmitted further. They must be dropped.
- keep - shows that priority must keep its current value (typically 0).
- default - means "for all remaining protocols" and allows to simplify significantly making the configuration file.
## To convert into an internal format:
cat my_dscp.txt|lst2dscp protocols.dscp
[SSG v13+] in input files of the lst2dscp utility, it is now possible to add comments (#) and empty lines.

To move the settings into the work directory:
mv protocols.dscp /etc/dpi/protocols.dscp
Please use mv instruction! It is an atomic one. Do not use copy!