# SWm Authorization Interface Settings
## Section "fast-epdg.auth"
Parameter	Description	Value
iface	Used interface	[SWm][SWx]

Template:
fast-epdg { auth { iface = swm {} swx {} s6b {} } }

## Section "fast-epdg.auth.swm"
Parameter	Description	Value
realm	Serviced realm	epc.mncYYY.mccXXX.3gppnetwork.org
host	Client hostname	epdg.epc.mncYYY.mccXXX.3gppnetwork.org
<diameter-aaa-server-name-1> {}	AAA Server #1 parameters
<diameter-aaa-server-name-2> {}	AAA Server #2 parameters
<diameter-aaa-server-name-n> {}	AAA Server #n parameters

Template:
fast-epdg { auth { iface = swm { realm = host = <server-name> {} } } }

Example:
fast-epdg { auth { iface = SWm swm { realm = epc.mnc002.mcc250.3gppnetwork.org host = epdg.epc.mnc002.mcc250.3gppnetwork.org <server-name> {} } } }

## Section "fast-epdg.auth.swm.<diameter-aaa-server-name-n>"
Parameter	Description	Value
priority	Balancing priority	0-100
local	Client address:port	IPv4: x.x.x.x:p, where x — a decimal number from 0 to 255, p — the client port IPv6: [y:y:y:y:y:y:y:y]:p, where y — a hexadecimal number from 0000 to FFFF, p — the client port
remote	AAA server address:port	IPv4: x.x.x.x:p, where x — a decimal number from 0 to 255, p — the AAA server port IPv6: [y:y:y:y:y:y:y:y]:p, where y — a hexadecimal number from 0000 to FFFF, p — the AAA server port
proto	Transport protocol	[sctp][tcp]

Template:
fast-epdg { auth { iface = swm { realm = host = diameter-aaa-server-1 { priority = local = remote = proto = tls = } diameter-aaa-server-2 { priority = local = remote = proto = tls = } } } }

Example:
fast-epdg { auth { iface = SWm swm { realm = epc.mnc002.mcc250.3gppnetwork.org host = epdg.epc.mnc002.mcc250.3gppnetwork.org diameter-aaa-server-1 { priority = 50 local = 192.168.1.1:3868 remote = 192.168.2.1:3868 proto = sctp tls = on } diameter-aaa-server-2 { priority = 50 local = 192.168.1.1:3869 remote = 192.168.2.2:3868 proto = tcp tls = off } } } }